## Slide 1: Lecture No. 22 Fuels
At the end of this lecture, students will be able to:
  Explain the Indian scenario of fuels
  Classify the fuels into primary and secondary source
  Discuss characteristic features of an ideal fuel
  Analyse a coal sample based on proximate and ultimate analysis

## Slide 2: Indian Scenario of Fuels
Energy is a basic need of every life on the earth
Energy is used in various forms such as mechanical energy, thermal energy, light energy, etc..
Used for various purposes such as domestic, transportation, manufacturing, etc.
Difficult to imagine life without energy

## Slide 3: Indian Scenario of Fuels
India is a country with more than 1.25 billion people accounting for more than 17% of world’s population
It faces a formidable challenge in providing adequate energy supplies to users at a reasonable cost
India’s nominal GDP crossed the US $ 2.308 trillion mark in 2014-15 which means that the annual growth rate of nominal GDP during the period is 7.3%
Ref: Journal of Sustainable Energy & Environment 3 (2012) 7-17

## Slide 4: Indian Scenario of Fuels
In the last six decades, India’s energy use has increased 16 times and the installed electricity capacity by 84 times
March 2015, energy consumption in India is the fourth biggest after China, USA and Russia
In recent years, India’s energy consumption has been increasing at a relatively fast rate due to population growth and economic development
Ref: Journal of Sustainable Energy & Environment 3 (2012) 7-17

## Slide 5
With rapid urbanization and improving standards of living for millions of Indian households, the demand is likely to grow significantly
By 2020, India will occupy the status of the 3rd largest energy consumer from its fourth position behind US, China and Russia currently
Despite having notable fossil fuel resources, the country has become increasingly dependent on energy imports
Ref: Journal of Sustainable Energy & Environment 3 (2012) 7-17
Indian Scenario of Fuels

## Slide 6: Indian Scenario of Fuels
Millions of Indian citizens have no access to frequent electricity
Over one third of India's rural population lacked electricity, as did 6% of the urban population
Of those who did have access to electricity in India, the supply was intermittent and unreliable
Blackouts and power shedding is interrupting irrigation and manufacturing across the country
Ref: Journal of Sustainable Energy & Environment 3 (2012) 7-17

## Slide 7: Indian Scenario of Fuels
Electricity sector in India had an installed capacity of 271.722 GW in the year 2014-15
Installed capacity became world's third largest in the year 2013 with 4.8% global share in electricity generation surpassing Japan and Russia
Non Renewable Power Plants constitute about 70% of the installed capacity, and Renewable Power Plants constitute the remaining nearly 30 % of total installed Capacity
Total annual generation of electricity from all types of sources was 1048.673 Billion Units in 2014-15
Ref: http://powermin.nic.in/power-sector-glance-all-india

## Slide 8: Indian Scenario of Fuels

## Slide 9: Chemical fuel and its Classification
Fuel + O2 → Products + Energy
(Hydrocarbon)
When the fuel undergoes combustion in air, carbon and hydrogen are converted into carbon dioxide and water respectively
Fuel is the carbonaceous substance that liberate enormous amount of energy upon combustion, which can be effectively used for domestic and industrial purposes

## Slide 10: How energy is produced?
Photo taken using X-ray laser at
Department of Energy’s SLAC
National Accelerator Laboratory to
get the first glimpse of the transition
state where two atoms begin to form a weak bond on the way to becoming a molecule
The reactants are a carbon monoxide molecule, left, made of a carbon atom (black) and an oxygen atom (red), and a single atom of oxygen, just to the right of it
Scientists Get First Glimpse of a Chemical Bond Being Born

## Slide 11: How energy is produced?
They are attached to the surface of a ruthenium catalyst, which holds them close to each other so they can react more easily
When hit with an optical laser pulse, the reactants vibrate and bump into each other, and the carbon atom forms a transitional bond with the lone oxygen, center
The resulting carbon dioxide molecule detaches and floats away, upper right producing energy

## Slide 12: Classification of fuel

## Slide 14: Proximate analysis
Proximate analysis refers to measuring moisture (M), volatile matter (VM), ash (A), and fixed carbon (FC) content in a coal is measured by the following equation
FC = 100 – (%M + %A + %VM)
Moisture is determined by drying 1 g of coal at 105°C for 1 hr
%M = (weight loss / weight of the sample) x 100
Ash is the weight of the residue obtained after complete combustion of 1 g of coal at 700-750°C
%A = (weight of residue / weight of sample) x 100

## Slide 15: Proximate analysis
Volatile matter is the weight loss obtained after heating 1 g coal sample at 950°C for 7 minutes in absence of air [VM consists of CO, H2, H2O, CO2, CH4, N2, O2, other hydrocarbons ]
Total weight loss of a moist coal = weight loss due to VM + Moisture
Weight loss due to VM = Total weight loss – moisture
If coal sample is dry, then weight loss is due to VM only
%VM = (weight loss due to VM / weight of sample) x 100

## Slide 16: Proximate analysis
Reporting Proximate analysis
Ex:
 | As received | Dry basis* | Dry-ash free basis** | Dry Mineral matter free***
%M | 6.8 | -- | -- | --
%A | 12.3 | 13.2 | -- | --
%VM | 36.2 | 38.84 | 44.7 | 44.6
%FC | 44.2 | 47.42 | 54.7 | 55.4
%S | 0.5 | 0.54 | 0.6 | --
Total | 100 | 100 | 100 | 100

## Slide 17: Proximate analysis

## Slide 18: Ultimate analysis
Ultimate analysis, which is more comprehensive, is dependent on quantitative analysis of various elements present in the coal sample, such as carbon, hydrogen, sulfur, oxygen, and nitrogen
Very important to material balance accurately
Carbon, hydrogen, sulfur, and nitrogen are calculated on experimental basis and expressed on moisture free basis
Then
  % Oxygen = 100 (%C + %H+ %N+ %S + %Ash)
  Note: Care must be taken while calculating to separate mineral matter such as CaO, MgO, SiO2, Al2O3, etc. from actual ash obtained from combustion of coal

## Slide 19: Ultimate analysis
Total Mineral matter (MM) can be calculated by Parr formula
MM = 1.08A + 0.55%S
Reporting Ultimate analysis:
Ex:

## Slide 20: Summary
  Classification of fuels: Primary, secondary
  Characteristics of a good fuel: Low ash, high CV, low moisture, moderate ignition temperature, etc.
  Coal analysis:
  Proximate analysis - measuring moisture (M), volatile matter (VM), ash (A), and fixed carbon (FC) content
  Ultimate analysis - quantitative analysis of various elements present in the coal sample, such as carbon, hydrogen, sulfur, oxygen, and nitrogen