## Slide 1: Lecture No. 24 Fuels
At the end of this lecture, students will be able to:
  Describe the cracking of petroleum and its significance
  Explain the fixed bed cracking of petroleum
  Discuss the fluidized bed catalytic cracking

## Slide 2: Cracking
Cracking is the process of breaking of higher molecular weight hydrocarbons (high boiling) to lower molecular weight hydrocarbons (low boiling) by the action of heat alone or heat in presence of a catalyst
C10H22 → C5H12 + C5H10
Decane n-pentane Pentene
(BP=1740C) (BP=360C)
Breaking of C-C and C-H bonds
It produces low boiling alkanes, alkenes and small amount of H2

## Slide 4: Thermal cracking
Liquid phase thermal cracking
Crude oil is pumped into the coil kept at 420-550 °C under a pressure of 15-100 kg/cm2
Better quality of gasoline is produced at this temperature
Gasoline with low octane value (60-70) is obtained which can be mixed with higher octane value gasoline and then used

## Slide 5: Vapour phase thermal cracking
Vapour phase thermal cracking
Heavy oil is heated in an heater at 400 °C to convert into the vapours
Vapours are passed to the reaction chamber which is maintained at 600-650°C and under the pressure of 10-20 kg/cm2
Higher hydrocarbon are converted into lower hydrocarbon easily and octane value to petrol is 75-80

## Slide 6: Catalytic cracking
Catalytic Cracking: Cracking of heavy oil in presence of catalyst
Fixed bed catalytic cracking
Fluidized (moving) bed catalytic cracking

## Slide 7: Fixed bed catalytic cracking

## Slide 8: Catalytic cracking
Fixed bed catalytic cracking:
Vapours of the heavy oil are heated in the presence of catalyst due to which a better yield of petrol is obtained
Working of Fixed bed catalytic cracking:
Heavy oil is vaporized by heating in electric heater and vapours are passed over a series of trays containing catalyst
Catalyst used are crystalline alumina-silicate, bentonite, bauxite and zeolites
Reaction chamber is maintained at 425-540 and under a pressure of 1.5 kg/cm2

## Slide 9: Fluidized bed catalytic cracking

## Slide 10: Fluidized bed catalytic cracking
Fluidized bed catalytic cracking ( moving bed)
Optimum conditions:
i) Feed stocks : Heavy oil fractions
Catalyst : Al2O3 + SiO2 (Alumino silicate, Finely
powdered form)
iii) Temperature : 5500C
iv) Pressure : 1-2 atm
Time : 3-4 sec
Production yield: 70%

## Slide 11: Reforming
Conversion of straight chain hydrocarbons into branched chain, cyclic and aromatic hydrocarbons, resulting in upgradation of petrol (improvement in octane number) is known as reformation
How reformation improves the quality of petrol?
1. Isomerization reaction:

## Slide 12: Reforming
2. Hydro cracking:
  Cracking of hydrocarbon in the presence of H2
  CH3-(CH2)5-CH3 + H2 → CH3-CH2-CH3 + CH3-CH2-CH2-CH3
  n-Heptane Propane Butane
  CH3-(CH2)8-CH3 + H2 → 2 CH3-(CH2)3-CH3
  Decane Pentane

## Slide 13: Reforming
3. Dehydrogenation reaction: Conversion of cycloalkane into aromatic compound

## Slide 14: Reforming
4. Dehydrocyclization reaction: Straight chain hydrocarbons undergo cyclization followed by dehydrogenation to produce aromatic hydrocarbons

## Slide 15: Summary
  Cracking of petroleum: Cracking is the process of breaking of higher molecular weight hydrocarbons (high boiling) to lower molecular weight hydrocarbons
  Fixed bed cracking of petroleum: Vapors of the heavy oil are heated in the presence of catalyst in fixed bed due to which a better yield of petrol is obtained
  Fluidized bed catalytic cracking: Vapors of the heavy oil are heated in the presence of catalyst in a fluidized bed reactor