## Slide 1: Lecture No. 25 Fuels
At the end of this lecture, students will be able to:
  Describe gasoline knocking in IC Engines
  Explain the role of octane number and cetane number
  Discuss the significance of anti-knocking agents

## Slide 2: Knocking
Knocking may be defined as the production of a shock wave in an IC engine as a result of an explosive combustion of fuel-air mixture, leading to a rattling sound
Compression ratio (CR) = V1/V2 = Volume of fuel air mixture at the end of suction stroke / Volume of fuel air mixture at the end of compression stroke
Higher the compression ratio, higher is the efficiency of an IC engine
CR is always greater than one since V1 being greater than V2

## Slide 3: Knocking in petrol engines:
Cause for knocking
http://www.animatedengines.com/otto.html
Working of four stroke petrol engine

## Slide 4: Knocking in petrol engines
Mechanism of knocking in chemical terms
Slow oxidation of the fuel (normal condition)
Slow combustion takes place due to the chain reaction

## Slide 5: Knocking in petrol engines
Chain reaction continues leading to aldehyde, decomposes to carbon dioxide and water

## Slide 6: Knocking Effects
Produces undesirable rattling sound
Increases the fuel consumption
Reduces the power output and hence the
efficiency of the engine
Causes mechanical damage due to overheating
to engine parts such as spark plug, piston and engine walls
Unpleasant driving

## Slide 7: Knocking Control
High octane gasoline
Low critical compression ratio
Anti-knocking agents such as TEL, TML, etc.
MTBE, ETBE, TMA, Amyl Alcohol

## Slide 8: Octane Number
Standard measure of a fuel’s ability to resist knock
Octane number is a measure of the knocking tendency of gasoline fuels in spark ignition engines
Percentage of iso-octane present in a standard mixture of iso-octance and n-heptane which has the same ignition properties as that of the petrol under examination
Octane number of a fuel is determined by measuring its knocking value compared to the knocking of a mixture of n-heptane and isooctane (2,2,4- trimethyl pentane)

## Slide 9: Octane Number
Example : If the octane number of a gasoline is 70
It means that it’s knocking characteristics are similar to that of the knocking characteristics of a mixture of 70% isooctane and 30% n-heptane
Order of octane no: Aromatic hydrocarbons > Alkenes > Cycloalkane > Branched chain alkanes > Straight chain alkanes

## Slide 10: Cetane number
Quality of diesel oil is measured in terms of its cetane number
Percentage of n-cetane present in a standard mixture of n- cetane and -methylnaphthalene which has the same ignition properties as that of the diesel under examination
-methylnaphthalene (C11H10) | n-cetane (n-hexadecane C16H34)
Cetane number=0 | Cetane number=100

## Slide 11: Cetane number
Example: If the cetane number of diesel oil is 80 it means that its ignition properties are similar to that of the ignition properties of a mixture of 80% n-cetane and 20% -methylnaphthalene
Cetane number can be improved by adding ethyl nitrate, acetone peroxide and amyl nitrate which helps in starting ignition
Cetane number of Aromatic hydrocarbons < Alkenes < Cycloalkane < Branched chain alkanes < Straight chain alkanes

## Slide 12: Anti knocking
Anti knocking agent:
Anti knocking agent is a chemical substance added to petrol to improve the anti knocking property of the petrol
For example:
  Tetra Ethyl Lead (TEL) (phased out)
  Tetra Methyl Lead (TML) (phased out)
  Methyl Tertiary Butyl Ether (MTBE) (additional oxygen in the ether moiety promotes efficient combustion)
  Ethyl Tertiary Butyl Ether (ETBE)
  Tetra Methyl Alcohol (TMA)
Disadvantages of leaded gasolines:
Pollutes the atmosphere
Lead poisons the rhodium catalyst which is used in catalytic converters

## Slide 13: Summary
    Gasoline knocking in IC Engines: production of a shock wave in an IC engine as a result of an explosive combustion of fuel-air mixture, leading to a rattling sound
    Role of octane number: Gives information on quality of petrol
    Cetane number: : Gives information on quality of diesel
    Significance of anti-knocking agents: Improves anti-knocking properties of petrol