## Slide 1: Lecture No. 30 Metallurgy
At the end of this lecture, students will be able to:
  Explain concentration of aluminum and copper
  Discuss the extraction and refining of aluminum and copper
  Describe the uses and properties of aluminum and copper

## Slide 2: Metallurgy of Aluminum
Occurrence of aluminum:
Aluminum is the third most abundant element in the earth crust
Next to oxygen and Silicon aluminum is more available (8.13 %)
Al has strong affinity towards oxygen so it is available in combined form than native form Al2O3.2H2O
Important aluminum ores:
Bauxite, Al2O3.2H20
(ii) cryolite, Na3AlF6
(iii) Feldspar, KAlSiO3O8
(iv) Mica, KAlSiO10 (OH)2
(v) Kaolinite, Al2Si2O7.2H2O

## Slide 3: Aluminum extraction from Bauxite
Bauxite, Al2O3.2H20 occurs as an impure form of aluminum oxide with TiO2, SiO2 and Fe2O3
Impurities like Fe & Si make aluminum brittle and prone to corrosion
First, the impurities from bauxite are eliminated using different methods such as Baeyer’s process, Hall’s process & Serpek’s process
Aluminum oxide can further be reduced to free aluminum at very high temperatures. But this method is not economical due to high affinity of aluminum for oxygen
Electrolysis is used to get pure aluminum from bauxite

## Slide 4: Purification-Baeyer’s Process
If ore contains appreciable amount of Fe2O3 this method is preferred to eliminate the impurities like Fe2O3 and SiO2 etc.
Pulverized and calcined ore is treated with hot and strong NaOH under pressure to form sodium meta aluminate
is in the solution and the impurities are undissolved, so filtration helps to separate impurities
This solution is cooled with excess water,
Aluminum hydroxide is further washed and heated to give pure alumina

## Slide 5: Purification-Hall’s Process
Low grade calcined bauxite is treated with Na2CO3 to produce sodium meta aluminate
Al2O3 + Na2CO3 → 2 NaAlO2 + CO2 ↑
is in the solution and the impurities are undissolved, so filtration helps to separate impurities
solution is heated with CO2 and excess water,
2 NaAlO2 + CO2 + 3H2O → 2Al(OH)3 ↓ + Na2CO3
Aluminum hydroxide is further washed and heated to give pure alumina

## Slide 6: Purification-Serpek’s Process
This method is used when bauxite contains appreciable amounts of silica
bauxite is mixed with carbon and heated up to 18000C in a current of nitrogen
Al2O3.nH2O + 3C + N2 → 2AlN + 3CO + nH2O
Aluminium nitride is hydrolyzed with hot water to give aluminum hydeoxide
AlN + 3H2O → Al(OH)3 ↓ + NH3
Aluminum hydroxide is further washed and heated to give pure alumina

## Slide 7: Electro-refining of Aluminum
Electrolysis of alumina yields pure aluminum but to further purify and get 99.99% purity electro-refining is performed
Bottom anode layer consists of impure aluminum
Middle layer consists of cryolite (Na3AlF6), alumina and barium fluoride acting as electrolyte
Top cathode layer consists of pure metal. This aluminum layer is connected with graphite electrode
Cell is made of iron box and is lined from inside with carbon

## Slide 8: Electro-refining of Aluminum
When electricity is passed aluminum from bottom layer moves to middle and further to top layer
At anode, Al Al3+ + 3e-
At cathode, Al3+ + 3e- Al (pure)
Pure aluminum is removed from the top & impurities are left behind
Pure aluminum is removed from the top and aluminum of lower purity is added to the bottom layer. Thus 99.99% pure aluminum is obtained using electro-refining

## Slide 9: Physical and Chemical properties of Aluminum
Physical properties:
Aluminum is a white metal which forms a protective oxide layer in moist air
It melts at 6580C and boils at 18000C
Aluminum is a good conductor of electricity and heat
Chemical properties:
Thin aluminum foil burns readily in air & forms oxide when heated
4 Al + 3O2 → 2Al2O3
Reaction with acids: 2Al + 6HCl → 2AlCl3 + 3H2
Reaction with base: Al + 2NaOH + 2H2O → 2NaAlO2 + 3H2

## Slide 10: Uses of Aluminum
Because aluminum is light and has high tensile strength, it is used to make automobiles and aircrafts
it is used for making electrical cables due to high electrical conductivity
it is used in making cooking utensils due to high thermal conductivity
used in thermite welding and in the aluminothermic process to reduce metal oxides into free metals
Used in paints, dyes etc.

## Slide 11: Metallurgy of Copper
Occurrence:
Copper is 25th most abundant element in the earth crust
It is available as a native element and also in combined form
Copper nuggets are largely exhausted
Mostly copper ores have bright colors
Important ores of copper:
Chalcopyrite, CuFeS2
Chalcocite, Cu2S
Covellite, CuS
Cuprite, Cu2O
Malachite, CuCO3.Cu(OH)2

## Slide 12: Extraction of Copper
Extraction of Cu from oxide ore:
Oxide ores are directly reduced to metallic copper by the reduction of carbon
Extraction of Cu from carbonate ore:
Ore is crushed and concentrated. Later, roasted in the presence of air which yields oxide of the metal
Oxide can be reduced by reduction with carbon
Δ
Δ
Δ

## Slide 13: Extraction of Copper
Extraction of Cu from sulphide ore:
Cu can be obtained by smelting process
Crushed and concentrated ore is heated in the presence of air
Copper and iron sulphides are further partially oxidized
Feo forms slag (FeSiO3) with silica and can be removed
Cu2S and Cu2O are allowed to react which forms metallic copper and SO2
When copper is cooled, SO2 slowly escapes from the surface leaving blisters on the surface of solidified copper which is known as blister copper
Δ

## Slide 14: Electro-refining of Copper
Anode is made of Impure copper (blister copper) and cathode is made of pure copper rod or sheet
Acidified CuSO4 solution is used as the electrolyte
At anode, Cu Cu2+ + 2e-
At cathode, Cu2+ + 2e- Cu (pure)
Many impurities settle down as sludge or mud below the anode (anode mud) & 99.99% pure copper can be prepared
(Pure Cu)

## Slide 15: Physical and Chemical properties of Copper
Physical properties of copper:
Copper is reddish brown colored and takes a bright metallic luster
It is malleable, ductile, and a good conductor of electricity and heat
Melting point is 1083°C and boiling point is 2567°C
Chemical properties of copper:
Reacts with oxygen in the atmosphere slowly and
forms a protective layer
Copper structures turn green in color
It tarnishes when exposed to some sulfur compounds

## Slide 16: Uses of Copper
Use to make electrical cables and electrical appliance
Used to make water pipes because if its inertness
It forms various alloys which are useful for many industrial processes
Copper compounds are used as insecticides, pesticides, pigments etc.
In many electrochemical processes copper is useful. It can be used as an electrode and used in techniques such as electroplating

## Slide 17: Summary
Aluminum is the third most abundant element in the earth crust
Bauxite, feldspar are the important ores of aluminum
Alumina is purified by different processes like Baeyer’s process, Hall’s process & Serpek’s process etc.
Pure alumina is used to produce aluminum metal by electrochemical methods
Aluminum is further purified by electro-refining
Copper is the 25th most available element in the earth crust
Chalcopyrite, Malachite, cuprite etc. ate the important ores of copper
Copper is extracted by pyrometallurgical methods and it is purified by electro-refining