## Slide 1: Lecture No.32 Metallurgy
At the end of this lecture, students will be able to:
  Explain the process of extraction of iron
  Discuss the purification of iron
  Describe the uses and properties of iron

## Slide 2: Metallurgy of Iron
Occurrence:
Next to ‘Al’ iron is the most abundant metal in earth’s crust
Iron is the 4th most abundant element
Iron has strong affinity to oxygen so it is not found in nature in the elemental state but only in combined state
Iron is often found as oxide
Important ores:
Haematite, Fe2O3
Limonite, Fe2O3.H2O
Magnetite, Fe3O4
Iron pyrites, FeS2
Siderite, FeCO3

## Slide 3: Commercial forms of Iron
(i) Cast or Pig iron – It is the most impure form of iron. It contains about 2.5 % to 4.5 % carbon. Other impurities like Si, P, Mn and S are present up to about 1.5 %
(ii) Wrought or Malleable iron – It is the purest form of iron. It contains
about 0.2 % carbon
(iii) Steel – It is an alloy of iron with carbon and other elements like manganese, silicon and phosphorus.
It is midway between cast and wrought iron as far as impurities are concerned.
It contains 0.1 to 1.5 % carbon

## Slide 4: Cast Iron
Cast iron is available in two forms,
(i) White cast iron:
Contains carbon as iron carbide, Fe3C and small amount of graphite
Obtained by cooling the molten pig iron quickly
(ii) Grey cast iron:
Contains carbon as graphite and small amount of Fe3C
Obtained by cooling molten pig iron slowly

## Slide 5: Cast Iron from Haematite
Concentration of ore:
Ore is crushed into small pieces of 3 to 5 cm size
Ore is washed with water to remove silicious impurities
Roasting the ore:
Ore is roasted with some amount of coal where following reactions take place
Water and CO2 are removed along with other impurities such as sulphur, arsenic, phosphorous
During smelting FeO will form slag as FeSiO3 but Fe2O3 will not

## Slide 6: Cast Iron from Haematite
Smelting:
Ore is mixed with flux (limestone) and coke in 8:1:4 ratio
In a blast furnace the mixture is heated
Charged from the top and hot air is sent from the bottom
After the reactions, waste gases are escaping from the top and molten metal along with slag are collected at the bottom

## Slide 7: Cast Iron from Haematite
From top to bottom temperature increases in the furnace
Moisture is removed in the first stage
At 400oC -700oC, oxygen reacts with coke and forms CO which further reduces the ore into spongy iron
CaCO3 is decomposed at high temperatures and form CaO which forms slag (CaSiO3) with SiO2 impurities
Slag floats over the molten iron layer and protects iron from oxidation
Molten iron is removed from the bottom and allowed to solidify which is called pig iron
Pig iron can be melted and cast in moulds which is called as cast iron

## Slide 8: Properties of Cast Iron
It is the most impure form of iron
Contains high amount of carbon
Melting point of cast iron = 1250oC; Melting point of pure iron = 1530oC
Cast iron has higher strength and hardness
But brittle in tension
It does not rust easily

## Slide 9: Properties of Cast Iron
When heated in air, it is oxidized and gets covered with thick bluish black scales of ferric oxide Fe3O4
When steam is passed over iron heated to 8000C to 10000C, iron is oxidized to Fe3O4
Acids form salts of iron
Fe + 2 H2SO4 → FeSO4 + SO2 + 2H2O
When heated with sulphur it forms ferrous sulphide and with dry chlorine it forms ferric chloride
Fe + S → FeS
2Fe + 3Cl2 → 2FeCl3

## Slide 10: Uses of Cast Iron
Car parts – cylinder heads, blocks and gearbox cases
Foundation for big machines (good damping property)
Pipes, lids (manhole lids)
Bridges, buildings
Cook wares – Excellent heat retention
Used to manufacture wrought iron and steel

## Slide 11: Wrought Iron
Purest form of iron with 0.12 to 0.25 % carbon and impurities like S, P, Mn etc. up to 0.3 %
It melts at a higher temperature ( 15000C) than cast iron
It is obtained by purifying cast iron by the process known as puddling (i.e. stirring)
Contains some amount of slag inclusions
Before steel production this was used extensively

## Slide 12: Wrought Iron from Cast Iron
Wrought iron is produced from cast iron by the process called puddling
Cast iron is heated in a special type of reverberatory furnace
Hot gases and flames are deflected by a low roof which can melt the cast iron and the molten iron is stirred or puddled by iron rods
Waste gases can escape through the chimney
Haematite lining
Cast iron

## Slide 13: Wrought Iron from Cast Iron
Furnace hearth is lined with haematite (Fe2O3) which provides oxygen to oxidize the impurities like C, S, Si, P, Mn etc.
C, S, Si forms oxides where as other impurities like Mn, P forms slags
Thus impurities are removed and pure wrought iron is obtained

## Slide 14: Properties of Wrought Iron
It is grey in color
It is soft, ductile and malleable
It is extremely tough and resistance against corrosion is high
Cab easily be welded and worked under hammer
Suitable for rolling and forging

## Slide 15: Uses of Wrought Iron
It is used to prepare chains, wires, bolts etc.
Railway couplings and carriages were made of wrought iron
It is used to manufacture articles which can withstand stress
Before the development of steel making wrought iron was the most commonly used malleable iron
In the past, wrought iron was refined into steel and used to make iron tools and weapons

## Slide 16: Summary
Iron is the 4th most abundant element
Haematite is the important ore of iron from which it is extracted
Cast iron or pig iron, wrought iron and steel are the commercial forms of iron
Haematite ore is heated at high temperatures in blast furnace and iron is melted
Impurities are separated as slag CaSiO3
Wrought iron is produced from cast iron by the process called puddling
It is the Purest form of iron with 0.12 to 0.25 % carbon
Cast iron is heated in a special type of reverberatory furnace and iron is melted where as impurities are oxidized and removed