## Slide 1: Lecture No. 35 Instrumental Methods of Analysis
At the end of this lecture, students will be able to:
  State Beer-Lambert’s law and its application in colorimetry
  Explain the observed spectra of colored solutions with reference to standard spectrophotometric chart
  Determine the concentration of an unknown colored solution using colorimetric data

## Slide 2: Block diagram of an instrumental measurement
  Classical Methods: Wet chemical methods such as precipitation, extraction, distillation, boiling or melting points, gravimetric and titrimetric measurements
  Instrumental Methods: Analytical measurements (conductivity, electrode potential, light absorption or emission, mass-to-charge ratio, fluorescence etc.) are made using instrumentation
Instrumental Methods of Analysis

## Slide 3
Chemical analysis involves identifying and determining the percentage composition of sample
Qualitative determining what species are present?
Quantitative determining how much of a species is present?
Sample under analysis is called analyte
Methods for quantitative are titrimetry (volumetry), gravimetry and instrumental methods
Instrumental Methods of Analysis

## Slide 4
Estimation of quantity of substance either by volumetry or gravimetry will not give accurate result
Volumetry: its not easy to get exact end point
Gravimetry: not easy to convert all ions or substance into precipitate
Instrumental: using a instruments to find quantity
Instrumental Methods of Analysis

## Slide 5
Principle:
An analytical instrument converts a property of a substance under investigation into an electric signal that can be measured by a suitable device
    Absorption of light
    Emission of light
    Changes in the concentration during redox and neutralization
Example : Colorimetry, potentiometry, conductometry
Instrumental Methods of Analysis

## Slide 6
Instrumental Methods of Analysis

## Slide 7: Colorimeter
Most common analytical technique used in biochemical estimation in clinical laboratory
Involves the quantitative estimation
Substance to be estimated should be colored or it should be capable of forming colored complex by the addition of reagents
Colored substance absorb light in relation to their color intensity
Color intensity will be proportional to the conc. of colored substance

## Slide 8: Electromagnetic spectrum
Notes: http://www.slideshare.net/biochem/colorimeter-ppt-biochemistry

## Slide 9: Colorimeter

## Slide 11: Colorimeter
Colored solutions have the property of absorbing certain wave length of light when a monochromatic light is passed through them
Amount of light absorbed or transmitted by a colored solution is in accordance with two laws: Beer’s law and Lambert’s law
Lambert’s law
Amount of light transmitted decreases exponentially with increase in path length (diameter) of the cuvette or thickness of colored solution through which light passes.
Beer’s law
When a monochromatic light passes through a colored solution, amount of light transmitted decreases exponentially with increase with increase in concentration of the solution

## Slide 12: Colorimeter
Beer-Lambert’s law
Amount of light transmitted through a colored solution decreases exponentially with increase in Conc of the colored and increase in path length of cuvette or thickness of the colored solution A = ЄCt Where ‘A’ is absorbance, ‘C’ is concentration, ‘t’ is thickness and ‘Є’ is a constant called molar extinction coefficient.
Є is constant for a given substance (it’s the absorbance of 1 mole solution of 1cm thickness)
Absorbance A of a medium is defined
  A = -log10T = log10P0/P
P0
P
t
Absorbing solution of concentration,C

## Slide 13
Transmittance is given by the equation:
T = I/Io
where I is the intensity of the light after it has gone
through the sample & Io is the initial light intensity.
Absorbance is related to the %T:
A = -logT = -log(I/ Io)
Transmittance is Related to Absorbance

## Slide 14
Equation Summary
T= (I/Io) = 10-A %T = (I/Io) x 100 A = -logT = log(1/T)
Note the scale for Absorbance: 9/10th of the scale is from 0-1 and 1/10th is from 1-2.
For this reason, the spectrometers have been calibrated in % Transmittance and
all readings will be taken in %Transmittance.
Sample Calculation
If %T = 95%, then A = log(100/95) = log(1/.95) = log(1.0526)
A = 0.02227

## Slide 15
Construction
Lamp emits all colors of light (i.e., white light).
Monochromator selects one wavelength and that wavelength is sent through the sample.
Detector detects the wavelength of light that has passed through the sample.
Amplifier increases the signal so that it is easier to read against the background noise.

## Slide 16: Working of colorimeter
Light from a light source passes through a Cuvette containing a solution sample
Some of the incoming light is absorbed by the solution
As a result, light of a lower intensity strikes a photodiode

## Slide 17: Colorimetric estimation of copper
Colorimetric estimation of copper in given unknown solution
Principle:
The absorbance of light of a particular wavelength by a substance in solution varies directly with its concentration and the thickness of the solution
When the thickness of the medium is kept constant, the absorbance directly depends upon the concentration
Experimental procedure :
Pipette out 2,4,6,8 and 10 cm3 of given copper sulphate solution into separate volumetric flasks
Add 2.5 cm3 of ammonia to each of them and also into the test solution of unknown concentration(ml)
Make it up to the mark (25 cm3 )and mix well

## Slide 18: Colorimetric estimation of copper
Measure the absorbance of each of these against blank solution (Only ammonia and water)
Plot a graph of absorbance (OD) against volume I concentration of cupric ions and determine the concentration of copper in the test solution
Reaction
Cu2+ (aq) + 4NH3 (aq) → [Cu(NH3)4] 2+ (aq)
Light blue Dark blue

## Slide 19: TABULATION AND CALCULATIONS:
Weight of copper sulphate pentahydrate present in 100 cm3 of the given solution = ‘X’ mg
Weight of CuSO4 .5H2O in 1 cm3 of its solution = X/100 mg =…………………… = ‘Y’ mg
Weight of copper present in 1 cm3 of its solution
REPORT:
Volume of unknown solution = …. cm3
Amount of copper in the given unknown solution = ………… mg

## Slide 20: Colorimeter
Limitation of beers lamberts law
Applicable only for monochromatic light
Only dilute solution

## Slide 21: Maintenance
Calibration
Adjustment
Replacement of burned-out lamp and photo detector
Electronic problems are rare

## Slide 22: Summary
  Beer-Lambert’s law
    Amount of light transmitted through a colored solution decreases exponentially with increase in Conc of the colored and increase in path length of cuvette or thickness of the colored solution
    A=ЄCt Determination of concentration of an unknown colored solution using colorimetric data