## Slide 1: Lecture No. 38
At the end of this lecture, students will be able to:
  Identify polymers based on physical properties - Homopolymers and copolymers
  Explain tacticity in polymers
  Nomenclature of a polymer

## Slide 2: Physical Properties
www.adhesiveandglue.com

## Slide 3: Elastomers
Materials which undergo recoverable deformation are called elastomers and exhibit rubber like elasticity
Elastomers → Long chain molecules with some cross-links
Cross-links keeps molecules from slipping past one another permanently
Relative mobility restricted to points between cross-links

## Slide 4
Cross-link points
Mobile segments
Elastomers

## Slide 5: Homo polymers and Hetero polymers
Homopolymers : All the repeating units (“mers”) are the same
-A-A-A-A-A-A-A-A-
Copolymer: polymer made up of 2 or more monomers
  Random copolymer: A-B-B-A-A-B-A-B-A-B-B-B-A-A-B
  Alternating copolymer: A-B-A-B-A-B-A-B-A-B-A-B-A-B
  Block copolymer: A-A-A-A-A-A-A-A-B-B-B-B-B-B-B-B
Homopolymer

## Slide 6: Copolymers
Copolymers : There is more than one type of repeating unit (“mer”) present.
Random copolymer
Alternating copolymer
Block copolymer
Graft copolymer
Homopolymer

## Slide 7: Examples of Homopolymers
polytetrafluoroethylene
PTFE – Teflon
poly(vinyl chloride) PVC
polypropylene PP
polyethylene
(polythene)

## Slide 8: Example of Copolymer

## Slide 9: Tacticity in polymers
Isotactic polymer:
All pendant groups are on the same side of the carbon chain

## Slide 10: Tacticity in polymers
Isotactic polymer:
All pendant groups are on the same side of the carbon chain

## Slide 11: Tacticity in polymers
Syndiotactic polymer:
Pendant groups alternate on either side of the carbon chain

## Slide 12: Tacticity in polymers
Atactic polymer:
Pendant groups oriented randomly

## Slide 13: Tacticity in polymers

## Slide 14: Structure
Handbook of Plastics, Elastomers, and Composites, 4th Edition Charles A. Harper (ed.)

## Slide 15: Classification of Polymers
Polymers
Chemistry Physical Prop. Size Shape Structure
Homo- Copolymers Linear Branched Cross-linked Network
polymers
Isomers
Thermo- Thermo- Elastomers
plastic setting
Stereo Positional Geometrical
Isotactic Syndiotactic Atactic cis trans

## Slide 16: Naming a Polymer
Subunit-based: To the name of the monomer the prefix poly is added, e.g. styrene → polystyrene; ethylene → polyethylene; propylene → polypropylene – simple homopolymers
Structure-based: IUPAC nomenclature is followed, based on the chemical structure, e.g. Polystyrene is poly(phenylethene); polyethylene is polyethene; polypropylene is poly(propene)
Bond-based: The prefix poly with the added name of the bond, e.g. polysiloxane for −O − Si − linkage. Used as a general umbrella term

## Slide 17: Naming a Polymer
Abbreviations: – most likely only capital letters, e.g.: PS for polystyrene; PMMA for polymethylmethacrylate; PTFE for polytetrafluoroethylene – very common and useful in literature, but needs to be defined and is not unique (e.g. PI can be polyisoprene or polyimide)
Trade names: – are used by industry or in daily life, e.g. Plexiglas for PMMA; Styrofoam for PS; Teflon for PTFE – the names have copyright protection and can describe complex polymer mixtures or a specially treated polymer
http://www.e13.physik.tu-muenchen.de/Muellerb/Uebung/chapter01.pdf

## Slide 18: Summary
  In this class we discussed the following:
Materials which undergo recoverable deformation are called elastomers and exhibit rubber like elasticity
Isotactic polymer: All pendant groups are on the same side of the carbon chain
Syndiotactic polymer:Pendant groups alternate on either side of the carbon chain
Atactic polymer: Pendant groups oriented randomly